## Slide 1: Techno-Economic Analysis of Decarbonization by Electrification of Recycle Processes for High-Purity Isopropanol Recovery
Yi-Xin Lo1, San-Jang Wang2，David Shan Hill Wong1*
1 Department of Chemical Engineering, National Tsing Hua University, Hsinchu, Taiwan

## Slide 2: Taiwan’s Long Term Decarbonization Roadmap
Actual emission 2022: 277 MT CO2e
https://www.ndc.gov.tw/Content_List.aspx?n=FD76ECBAE77D9811&upn=D34BDBBBF9103806
Notes: This is our government plan for march towards the zero emission target.
The original commitment is 50% reduction by 2050 is revised to Net Zero.
The short term target calls 50 MT reduction by 2030.
The latest data of 2022 showed no reduction at all.
Please be reminded that I am not making any judgement on the planning.
Part of responsibility of failure has to be laid on us, the practicing community.

## Slide 3: Methods of Decarbonization
Present-to-2030
  Phase out old equipment
  Intelligent operation
  Fuel switching from coal to natural gas/hydrogen
2030-to-2050
  Integration of renewable power
  Revamping of utility system
Limited reduction of CO2e
Deep decarbonization
How should process adapt?
Notes: Our government plan actually comes with a working plan for our chemical industry.
Deep decarbonization is achieved by Integration of renewable power and revamping of utility system

## Slide 4: Heat Based vs Electricity Based Process
In the future, a great portion of energy is in the form renewable electricity from renewable energy based grid, or utility system.
A great portion of current process energy demand is in the form of steam, generated by a fossil fuel based utility system
Carbon based Utility System
Coal
Natural Gas
Fuel Oil
…
Production Process
Grid
Steam supply
Electricity supply
RE based Utility System
Renewable Electricity
Production Process
Low Carbon Grid
Steam supply
Electricity supply
It is unreasonable, thermodynamically, to convert electricity back into heat. Increasing direct electricity use in a process system, is imperative.
Notes: A great portion of current process energy demand is in the form of steam, generated by a fossil fuel based utility system
In the future, a great portion of energy is in the form renewable electricity from renewable energy based grid, or utility system.
It is unreasonable, thermodynamically, to convert electricity back into heat. Increasing direct electricity use in a process system, is imperative.

## Slide 5: Energy Consumption of Separation Process and Distillation
Separation is a nonspontaneous process, work is required.
Sholl and Lively 2016 reported separation processes consumed nearly 16% percent of total US energy consumption.
Distillation is the workhorse separation process and consumes about half of all energy consumed by separation processes.
How should distillation switched from a thermal-driven to a electric-driven process and what is the cost?
Sholl, D. S., & Lively, R. P. (2016). Seven chemical separations to change the world. Nature, 532(7600), 435-437.
Notes: Separation is a nonspontaneous process, work is required.
Sholl and Lively 2016 reported separation processes consumed nearly 16% percent of total US energy consumption.
Distillation is the workhorse separation process and consumes about half of all energy consumed by separation processes.
How should distillation switched from a thermal-driven to a electric-driven process and what is the cost?

## Slide 6: Motivation, Scope and Objective
High purity isoproanol IPA (IPA, >99.97%) is a feedstock for electronic grade IPA, which is an important solvent for semiconductor manufacturing.
High purity IPA recovery from (IPA, >99.97%) from spent IPA (~15%) is an important part of circular economy for semiconductor manufacturing industry.
The processes have been studied well in the literature, but they are all energy intensive.
Decarbonization of three high purity IPA recovery processes by electrification will be presented in this study.
The goal is to demonstrate the economic potential of this pathway to net zero

## Slide 7: Methods of Electrification
Electric Furnace/Boiler (EF/EB)
Heat-pump assisted distillation (HPAD)
  Mechanical Vapor Recompression (MVR)
  Bottom Vapor Flash Compression (FVC)
  Organic Rankine Cycle (ORC)
Steam Generation Heat Pump (SGHP)
MVR+EB, SGHP will be used in this work

## Slide 8: Steam Generaltion Heat Pump
COP of generating low pressure steam from process vapors ranges from 5.5~13.3, we adopt the low estimate of 5.5
COP of generating high pressure steam ranges from waste heat3.5~10.3, we adopt the low estimate of 3.5
COP of generating high pressure steam from process vapors is esimated to be 2.1
Klute et al, Steam generating heatpumps-overview,classification,economics,and basic modeling principles.Energy Conversionand Management,299:117882,202
TRL>9
Notes: The table lists a variety of SGHP working fluids and their application conditions, and indicates the COP values and steam temperature ranges of different systems. For example, EPCON's MVR heat pump used in this study has a COP of about 5.5 for low to medium temperature (<150°C) applications, while the Spilling steam compressor raises the steam temperature to 250°C with a COP of about 3.5, and steam generation above 250°C requires a series cascade of two SGHPs, with a combined COP of about 2.1.

## Slide 9: Technoeconomic Data
Data compiled from Taipower, Energy Bureau, Ministry of Economics, IEA, IRENA, IPCC and other open source literature
Notes: Calculations for each energy source are as follows: (a) Heat production cost and emissions from coal: based on imported thermal coal at US$120/ton, with a heat value of about 7,000 kWh/ton, and after correcting for the boiler efficiency, the unit price of heat is about US$0.03/kWh, and the carbon dioxide emissions are about 0.55 kgCO2/kWh. (b) Heat production cost and emissions from liquefied natural gas (LNG): the price of LNG is about US$14/MMBtu, which translates into a unit price of heat of about US$0.08/kWh and carbon dioxide emissions of about 0.32 kgCO$_2$/kWh. MMBtu, converted heat unit price about US$0.08/kWh, and CO2 emissions about 0.32 kgCO$_2$/kWh.(iii) Renewable electricity (wind): electricity price about US$0.055/kWh, and lifecycle emissions about 0.10 kgCO2e/kWh.(iv) Small Module Nuclear Energy (SMR) (d) Small Module Nuclear (SMR): electricity price about US$0.095/kWh, life cycle emission about 0.01 kgCO2e/kWh.(e) Taiwan Grid Power: industrial electricity price about US$0.143/kWh, average carbon emission factor about 0.50 kgCO2e/kWh. The above data are summarized in the table to provide a basic basis for the analysis of the cost of energy and the carbon emission in the future.

## Slide 10: Azeotropic Distillation Using Cycohexane
Wang, C. J., Wong, D. S. H., Chien, I. L., Shih, R. F., Liu, W. T., & Tsai, C. S. (1998). Critical reflux, parametric sensitivity, and hysteresis in azeotropic distillation of isopropyl alcohol+ water+ cyclohexane. Industrial & engineering chemistry research, 37(7), 2835-2843.
Chien, I. L., Wang, C. J., Wong, D. S. H., Lee, C. H., Cheng, S. H., Shih, R. F., ... & Tsai, C. S. (2000). Experimental investigation of conventional control strategies for a heterogeneous azeotropic distillation column. Journal of Process Control, 10(4), 333-340.
Shi, L., Huang, K., Wang, S. J., Yu, J., Yuan, Y., Chen, H., & Wong, D. S. (2015). Application of vapor recompression to heterogeneous azeotropic dividing-wall distillation columns. Industrial & Engineering Chemistry Research, 54(46), 11592-11609.

## Slide 11: Basic Three Column Process
Notes: In this study, th steady state simulation of a three-column azeotropic distillation system (CyH_AD) was carried out using Aspen Plus V12.1, and the process configuration is shown in the figure. The feed was a 15 wt% isopropyl alcohol (IPA) solution in circulating water with a flow rate of 7 tons per hour. The feed first enters the preconcentration column (C1) to increase the concentration of IPA, and then flows into the azeotropic column (C2), where cyclohexane (CYH) is added as an azeotropic agent to form a ternary lowest boiling point azeotropic mixture of water, IPA and CYH. After condensation, the vapor at the top of the tower is separated into CYH-rich phase and water-rich IPA phase, where the CYH-rich phase is refluxed to replenish the azeotropic agent, and the water-rich IPA phase is sent to the dewatering column (C3) for further drying.The product at the bottom of the C2 tower reaches a purity of 99.97 wt% of IPA, w

## Slide 12: HPAD Design
Notes: The heat pump-assisted three-column azeotropic distillation (HPAD) system is based on the principle of mechanical vapor recompression (MVR), which is based on the compression of steam at the top of the distillation columns and the recovery of its latent heat of condensation to supply the reboiler load to form a closed-loop, self-feeding heat pump cycle in each distillation column. The complete flow of the system is shown in the figure. The system integrates two independent heat pump circuits. C1 tower top vapor is compressed by single-stage isentropic compression, the pressure is raised from 1 atm to 2.981 atm, part of which is supplied to C2 tower, and the rest is completely condensed at 2.981 atm and 110°C, and the latent heat of condensation is supplied to the C1 reboiler directly to form a closed-loop heat recovery. C2 tower top vapor is compressed to 6.1 atm, and condensed at 114°C, the released heat energy can also satisfy the load of each distillation tower. The heat released meets the demand of both C2 and C3 reboilers. Due to the compression ratio of 6.1, the compression process is divided into two stages in consideration of thermal efficiency and mechanical constraints. An intercooler is provided between the two stages to partially condense the superheated vapor at 111°C, effectively recovering the sensible heat and supplying it to the C1 reboiler. Since the recovered heat from vapor recompression is not enough to fully supply the heat load of C1 and C2, auxiliary electric boilers (EB1 and EB2) are installed at the bottom of the two towers to supplement the heat energy.

## Slide 13: SGHP Processs (COP=5.5)
Notes: The temperature of the tower bottom is below 150c, so the centralized heat supply is provided by a steam heat pump system (SGHP) with a COP of 5.5. The system converts the original heat load of about 1,892 kW into an electrical power input of 344 kW, which significantly improves energy efficiency. A schematic diagram of the system flow is shown in the figure.

## Slide 14: Economic Analysis
Carbon abatement cost is calculated with reference to conventional process with coal as fuel
 | Conventional |  | HPAD+EB |  |  | SGHP |  | 
Energy Type | Coal | LNG | Wind | SMR | GRID | Wind | SMR | GRID
Energy [kW] | 4441(Q) |  | 1862(W) |  |  | 807(W) |  | 
Energy Cost [USD/h] | 133 | 355 | 102 | 177 | 266 | 44 | 77 | 115
CO2e[kg/h] | 2443 | 1421 | 186 | 19 | 931 | 81 | 8 | 404
Caron Abatement Cost [USD/tonCO2] | -- | 217 | -14 | 18 | 88 | -38 | -23 | -9
Notes: In this slide, the economic benefits and costs of the conventional three-column azeotropic distillation, a heat pump-assisted distillation coupled with an assisted electric boiler system (HPAD+EB), and a steam-generated heat pump (SGHP) system with a COP of 5.5 are compared. The CAC is calculated to is calculated with reference to conventional process with coal as fuel

## Slide 15: Azeotropic Distillation using Di-isopropyl Ether (DIPE)
Qi, J., Tang, J., Zhang, Q., Wang, Y., Chen, H., Zhao, H., & Zhang, L. (2019). Heat-integrated azeotropic distillation and extractive distillation for the separation of heterogeneous ternary azeotropes of diisopropyl ether/isopropyl alcohol/water. Industrial & Engineering Chemistry Research, 58(45), 20734-20745.

## Slide 16: Two-Column Process
Notes: A two column process was simulated. The total condenser duty was found to be 1675 kW and the total reboiler duty was found to be 1894 kW.

## Slide 17: HPAD Process
Notes: In HPAD the total work required is reduced to 268 kW, yet two electric reboilers of 360 kW are required

## Slide 18: SGHP Process (COP=5.5)
Notes: The work of SGHPs were computed using a COP 5.5

## Slide 19: Economic Analysis
Carbon abatement cost is calculated with reference to conventional process with coal as fuel
 | Conventional |  | HPAD+EB |  |  | SGHP |  | 
Energy Type | Coal | LNG | Wind | SMR | GRID | Wind | SMR | GRID
Energy [kW] | 1892(Q) |  | 628(W) |  |  | 544(W) |  | 
Energy Cost [USD/h] | 57 | 151 | 35 | 60 | 90 | 19 | 33 | 49
CO2e[kg/h] | 1041 | 605 | 63 | 6 | 314 | 34 | 3 | 172
Caron Abatement Cost [USD/tonCO2] | -- | 216 | -22 | 3 | 45 | -38 | -23 | -9
Notes: In this slide, the economic benefits and costs of the conventional three-column azeotropic distillation, a heat pump-assisted distillation coupled with an assisted electric boiler system (HPAD+EB), and a steam-generated heat pump (SGHP) system with a COP of 5.5 are compared. The CAC is calculated to is calculated with reference to conventional process with coal as fuel

## Slide 20: Extractive Distillation Using Dimethyl Sulfoxide
Arifin, S., & Chien, I. L. (2008). Design and control of an isopropyl alcohol dehydration process via extractive distillation using dimethyl sulfoxide as an entrainer. Industrial & engineering chemistry research, 47(3), 790-803.
Liang, K., Li, W., Luo, H., Xia, M., & Xu, C. (2014). Energy-efficient extractive distillation process by combining preconcentration column and entrainer recovery column. Industrial & Engineering Chemistry Research, 53(17), 7121-7131.
Duan, C., & Li, C. (2023). Energy-saving improvement of heat integration for separating dilute azeotropic components in extractive distillation. Energy, 263, 125821.

## Slide 21: Without Heat Integration

## Slide 22: Conventional Process (ED_DMSO)
Notes: The total condenser duty available is 1383 kW, the total reboiler duty required is 1629 kW, again the duty provided is insufficent

## Slide 23: HPAD Design ED_DMSO+HPAD
Notes: Two electric boilers are required
The total worj required is 113+61+43+69+84+3.5+94+81=708

## Slide 24: SGHP Process (ED_DMSO+SGHP)

## Slide 25: SGHP Process (ED_DMSO+SGHP)

## Slide 26: Economic Analysis
Carbon abatement cost is calculated with reference to conventional process with coal as fuel
 | Conventional |  | HPAD+EB |  |  | SGHP |  | 
Energy Type | Coal | LNG | Wind | SMR | GRID | Wind | SMR | GRID
Energy [kW] | 1629(Q) |  | 704(W) |  |  | 509(W) |  | 
Energy Cost [USD/h] | 49 | 130 | 39 | 67 | 101 | 28 | 48 | 73
CO2e[kg/h] | 886 | 521 | 70 | 7 | 352 | 51 | 5 | 255
Caron Abatement Cost [USD/tonCO2] | -- | 216 | -12 | 20 | 96 | -25 | -1 | 37
Notes: In this slide, the economic benefits and costs of the conventional three-column azeotropic distillation, a heat pump-assisted distillation coupled with an assisted electric boiler system (HPAD+EB), and a steam-generated heat pump (SGHP) system with a COP of 5.5 are compared. The CAC is calculated to is calculated with reference to conventional process with coal as fuel

## Slide 27: Heat Integration

## Slide 28: Conventional Process (DMSO_ED+HI)

## Slide 29: HPAD Design (ED_DMSO_HI+HPAD)

## Slide 30: SGHP Process (ED_DMSO_HI+SGHP)
COP=5.5 for C1
COP=2.1 for C2&C3

## Slide 31: Economic Analysis
Carbon abatement cost is calculated with reference to conventional process with coal as fuel
 | Conventional |  | HPAD+EB |  |  | SGHP |  | 
Energy Type | Coal | LNG | Wind | SMR | GRID | Wind | SMR | GRID
Energy [kW] | 737(Q) |  | 622(W) |  |  | 351(W) |  | 
Energy Cost [USD/h] | 22 | 59 | 34 | 59 | 89 | 19 | 33 | 50
CO2e[kg/h] | 405 | 236 | 62 | 2 | 311 | 35 | 4 | 176
Caron Abatement Cost [USD/tonCO2] | -- | 216 | 35 | 93 | 713 | -8 | 27 | 122

## Slide 32: Conclusions

## Slide 33: CO2 emission
Deep carbon abatement can be achieved by electrification with SGHP and HPAD

## Slide 34: Energy Cost
For SGHP, reduction in energy cost can be achieved regardless of the low carbon energy source except for the ED_DMSO_HI case.
For HPAD, reduction in energy cost can only be achieved by wind power. For ED_DMSO_HI case no reduction is possible.

## Slide 35: Carbon Abatement Cost
For SGHP, negative carbon abatement costs except for and ED_DMSO using grid power and the ED_DMSO_HI case.
For HPAD, negative carbon abatement costs cost can only be achieved by wind power. For ED_DMSO_HI case the carbon abatement costs are all possible.

## Slide 36: Overall Summary
Electrification offers great potential for deep decarbonizaton
It is less costly to fuel switching and carbon capture.
Negative carbon abatement costs, or benefits can achieved in some cases; providing incentives for process industry to start investing in this technology.
SGHP is in generable more flexible than local HPAD, only revamping of the utility system is required.